## Slide 1: Preliminary Design Review (PDR)
Charger Rocket Works
University of Alabama in Huntsville
NASA Student Launch 2013-14
Kenneth LeBlanc (Project Lead)
Brian Roy (Safety Officer)
Chris Spalding (Design Lead)
Chad O’Brien (Analysis Lead)
Wesley Cobb (Payload Lead)

## Slide 2: Prometheus Flight Overview
Event | Value | Units
Max Speed | 1960 | ft/s
Time To Apogee | 24.9 | s
Apogee | 14800 | ft
Time at Main Deploy | 176 | s
Main Chute Deployment Altitude | 1000 | ft
Ground Impact Speed | 7.0 | ft/s
Nose Cone Impact Energy | 0.83 | ft-lbf
Body Impact Energy | 15.9 | ft-lbf

## Slide 3: Project Schedule

## Slide 4: Outreach
Under Construction
Modular in Nature
Adaptable for different ages and lengths
Supporting activity
  Water Rockets
  Drag Experiment
Packet format for easy integration into existing events

## Slide 5: Materials and Justifications
Component | Material | Justification
Body Tube | Carbon Fiber | High strength requirement, ease of fabrication, student learning experience
Fins | Carbon Fiber | High strength requirement, ease of fabrication, student learning experience
Bulkheads | Carbon Fiber | High strength requirement, ease of fabrication, student learning experience
Nose Cone | Fiberglass | Radio transparency, moderate strength requirement
Payload Bays | 3D Printed ABS | Low strength requiement, low weight, complex profiles possible
Payload Shaft | Alumium | Low weight, threaded shaft required

## Slide 6: Vehicle Component Discussion
Body Tube
  4.5” inside diameter
  Wrapped carbon fiber tube
    Carbon cloth wrapped over mandrel
    High strength, ease of fabrication

## Slide 7
Vehicle Component Discussion
Payload Shaft
  3/8” Aluminum Thread
    Threaded into motor case end cap
    Passes thrust/ recovery forces into bulkhead, payloads, etc
    Retains body tube segments

## Slide 8
Vehicle Component Discussion
Fins
  Carbon fiber
    Nanolaunch profile
    Two piece design allowing large flange fabrication

## Slide 9: Vehicle Component Discussion
Nose Cone
  Fiberglass
    Nanolaunch Profile
    Will include Nanolaunch payload components

## Slide 10: Next Steps
Hardware
  Materials and Structures Testing
  Design Refinement
  Subscale and Prototype Fabrication

## Slide 11: Launch Vehicle Verification
Tension tests of materials samples
  Control samples and samples heated to temperatures shown in supersonic CFD analysis
    Confirms suitability of standard epoxy for short bursts at supersonic temperatures
Compression tests to failure of representative high stress components
  Confirms design calculations
Proof loading of actual flight hardware
  Non destructive
  Confirms strength of critical, difficult-to-inspect epoxy joints

## Slide 12: Static Stability Margin
OpenRocket simulated CG and CP
Vehicle is stable
Supersonic flight
  Xcp expected to grow
  Xcg expected to shrink
  Stability expected to increase

## Slide 13: Baseline Motor Selection
Cessaroni Technology Incorporated - 7312 M4770-P
3 Grain
High Impulse (7,312 N-s)
Low Burn Time (1.53 seconds)
Thrust to Weight Ratio (36.5)

## Slide 14: Projected Flight Path
Chart: Mission Trajectory Profile
Event | Value | Units
Total Flight Time | 249 | sec

## Slide 15: Ascent
Chart: Vehicle Ascent Profile
Event | Value | Units
Time To Apogee | 24.9 | seconds
Apogee | 14800 | ft

## Slide 16: Powered Flight
Event | Value | Units
Burn Time | 1.53 | seconds
Burn Out Altitude | 1500 | feet
Burn Out Velocity | 1900 | fps
Max Acceleration | 43 | G’s
Chart: Vehicle Acceleration Profile

## Slide 17: Descent
Event | Value | Units
Drogue Release | 26 | seconds
High Altitude Descent Speed | 100 | ft/s
Main Release | 1000 | ft
Low Altitude Descent Speed | 7 | ft/s
Impact Energy Bottom Section | 15.9 | lbf
Impact Energy Nose Cone | 0.83 | lbf
Chart: Descent

## Slide 18: Mass Variance Analysis
Chart: Altitude Variance with Launch Mass
Monte Carlo Method
150 Test Cases
Chart: Speed Variance with Launch Mass
Chart: Acceleration Variance with Mass

## Slide 19: Next Steps
Analysis
  CFD-ACE+ Fluid Dynamics Models
  Post Flight Analysis
  Generate a 6-axis Flight Trajectory Model using Commercial Software

## Slide 20: Payload Systems
Dielectrophoresis
Effects of Supersonic Flight on Paints/Coatings
Landing Hazard Detection System
Nanolauch 1200 Experiment

## Slide 21: Baseline Payload Design
Segmented modular design
Customizable
Able to be arranged for CG
Can be inserted and removed in one piece
Consolidated
Easy Maintenance
Designed to account for high G-forces

## Slide 22: Payload Verification and Test Plan
Payload Requirement | Design Capability | Risk | Metric/Verification
Administer High Voltage Dielectric Test | Provide same voltage as previous experiments | Electric shock or dielectric failure | Post flight video inspection and buzzer sounding to indicate voltage is on.
Microgravity | Experience a second of low g to run experiment | Not enough time to see clear results | Post-flight video inspection
Coatings and Paint | Two different coatings/ paints for analysis | Rocket appearance could change depending on the paint’s reaction to the heat. | Visual inspection of surface roughness changes, most heat resistant, and durability of coating
Preflight Post flight surface analysis | Optical microscope analysis of the surface before and after flight | Deterioration of initial paint/coating due to high heat | Pre-flight vs Post-flight inspection/analysis comparison at microscopic level

## Slide 23: Payload Verification and Test Plan
Payload Requirement | Design Capability | Risk | Metric/Verification
Hazard detection camera | Hang a camera below the rocket on descent | Camera tangles up with the shock cord or parachute, and/or blocks the camera view | Camera deploys safely and analyzes the landing zone
Live Data Feed | Recording data if the ground below is clear of hazards | Camera results could be inconclusive due to swaying motion of parachute | Ground station receives live conclusive evidence of landing hazards
Recoverable and Reusable | Capable of being launched again on the same day without repairs or modifications | All or some of the systems/subsystems destroyed due to recovery failure | All payload components recovered, and in working condition

## Slide 24: Next Steps
Avionics and Payload
  Payload Sled Fabrication and Strength Test
  Component Calibration and Testing
  LHDS Development
  Nanolaunch Program Code

## Slide 25
Question
&
Answer